## Slide 1
RV Belgica
A new multidisciplinary research vessel to replace the RV A962 Belgica
Lieven Naudts
RBINS – OD Nature
Royal Belgian Institute of Natural Sciences – Operational Directorate Natural Environment

## Slide 2
Timeline
Design phase
Building phase
Overview

## Slide 3
2018-2020
Pre-June 2018 See poster and previous ERVO presentations (2005 - 2018)
June 2018 Signed contract (= tender + offer & notification)
2018-2019 Design phase (8 months) incl. setup onsite team
2018-2019 Name-giving competition (high school students 12-16 years): RV Belgica
2019-2020 Building phase (20 months)
2019-2020 Procurement private operator (mixed crew: military & civil)
2019-2020 New operational convention and business plan (Council of Ministers)
Autumn 2020 Delivery new RV Belgica
Timeline

## Slide 4
Full Ocean Research Vessel
71.4 m length, 16.8m beam, max. 4.8 draft (cfr. coastal monitoring)
11 kn operational speed (max. 13 kn)
Able to deploy wide range of scientific gear up to 5000 m water depth
North Sea, Atlantic Ocean, Mediterranean Sea
Ice Class for summer operations in Arctic areas
Class: DNV-GL ✠1A; ICE-1C; SPS; E0; DYNPOS(AUTR); COMF-V(2); COMF-C(2); BWM-T; TMON; Silent-R; NAUT(AW)
Design phase

## Slide 5
Silent Research Ship – Green Ship
Diesel-Electric propulsion (AC) (3*ABC – Rolls-Royce + 2* Indar; twin screw – 5-blade – fixed pitch)
DNV-GL Silent-R
MARPOL TIER III
Waste-heat recovery
Energy-saving alternatives
Design phase
2*1200 kW
2*535 kW
2*730 kW
2*1780 kW
1*1335 kW

## Slide 6
New capabilities
Dynamic Positioning Class 2 (DP-2) (2 stern & 2 bow thrusters)
Hoppe roll reduction system
12 crew – 28 scientists & marine technicians (14 single - 13 double cabins)
30 day autonomy
300 days/year at sea (operating cost 4,3 M€/year incl. VAT)
Design phase

## Slide 7
Space for science
Crow’s Nest (8 m2)
Operational Center (60 m2)
Scientific Lab / Conf. Room (51 m2)
ICT Room (26 m2)
Wet Lab (46 m2)
3 Dry Labs (19 & 40 & 33 m2)
CTD hangar (23 m2)
Science Hangar (78m2,place for 2 ISO 20’ containers)
Large AFT & STBD decks (place for 5 ISO 20’ containers)
Diver Store (7 m2)
Seismic Room (6 m2)
Wet and Dry Fish Lab (68 & 21 m2)
Cold & Freeze Rooms (14 & 14 m2)
Aerosol Lab (9 m2)
AUMS Lab (16 m2)
Lab surface: 410 m2
Hangar surface: 101 m2
Deck surface: 218 m2 + 34 m2 + 83 m2
Design phase

## Slide 8
Design phase
Deck below Bridge Deck (deck 6)

## Slide 9
Design phase
Scientific Lab / Conference room (preliminary design)

## Slide 10
Design phase
Main deck (deck 4)

## Slide 11
Design phase
Deck below main deck (deck 3)

## Slide 12
Space for science
Crow’s Nest (8 m2)
Operational Center (60 m2)
Scientific Lab / Conf. Room (51 m2)
ICT Room (26 m2)
Wet Lab (46 m2)
3 Dry Labs (19 & 40 & 33 m2)
CTD hangar (23 m2)
Science Hangar (78m2,place for 2 ISO 20’ containers)
Large AFT & STBD decks (place for 5 ISO 20’ containers)
Diver Store (7 m2)
Seismic Room (6 m2)
Wet and Dry Fish Lab (68 & 21 m2)
Cold & Freeze Rooms (14 & 14 m2)
Aerosol Lab (9 m2)
AUMS Lab (16 m2)
Lab surface: 410 m2
Hangar surface: 101 m2
Deck surface: 218 m2 + 34 m2 + 83 m2
Design phase

## Slide 13
Winches, Cranes & Frames
3 Cranes (FWD, MID, AFT) – 1.5t, 4t, 8t @16m
2 CTD Winches (STBD) – AHC – 2.9t – 5500m
Multifunctional Winch (STBD) – 9t – 5500m
Hydrographic Winch (AFT/STBD) – 5.2t – 5500m
2 Trawl Winches – 40.2t – 5500m
Net Drum Winch – 40.4t – 10m2
Split Net Drum Winch – 30.2t – 8m2 each
Net Sonde Winch – 4.2t – 5500m
2 Gilson Winches – 10.5t – 5500m
CTD Gantry & LARS (STBD) – 4.9t
2 STBD T-frame Gantries – 15t
AFT A-Frame – 30t
Work Boat – 7 m
Piston corer incl. LARS solution – 15 m
  Able to deploy wide range of scientific gear up to 5000 m water depth
Design phase

## Slide 14
Winches, Cranes & Frames
Design phase
Deck above main deck (deck 5)

## Slide 15
Full Acoustic Underwater Instrumentation suite
Shallow (EM2040) and deep-water (EM304) bathymetric multibeam echosounders (600 m & 8000 m)
Parametric subbottom profiler (Topas PS18) (11000 m)
Scientific multibeam (ME70) & split-beam wideband echosounder (EK80) (>5000 m)
Omnidirectional fish sonar (SU90) (4500 m)
Net- and catch monitoring system (PX & FX80)
Underwater position-reference system (USBL) (HiPAP 502) (5000 m)
Acoustic Doppler Current Profilers (Ocean Surveyor 75 kHz & Workhorse 600 kHz) (1000 m & 50 m)
  Mapping and analyses of full water column (incl. fauna), sea floor and subsurface
Design phase

## Slide 16
Adapted to existing large European Marine Research Infrastructure
As a requirement of full list of embarkable infrastructure was given:
  Autonomous Underway Vehicles (AUVs) (Hugin, AutoSub, etc.)
  Remotely Operated Vehicles (ROVs) (Victor 6000, Holland I, Quest, Kiel 6000, etc.)
  2D & 3D seismic systems (Ifremer, P-Cable)
  Scientific sediment coring and rock drill devices (RD2, MeBo70, etc.)
  Storage space for 7 ISO 20’ containers AFT + 2 ISO 20’ container FWD
  2 integrated drop keels
  UAV platform FWD
  A platform for European cooperation through which Belgian researchers get access to large European marine research infrastructure
Design phase

## Slide 17
Adapted to existing large European Marine Research Infrastructure
ROV Victor 6000
Large effort by the yard, designer, deck machinery supplier, NewRV team…
and with the help of foreign colleagues!!
Design phase

## Slide 18
Adapted to existing large European Marine Research Infrastructure
BGS RD2
Large effort by the yard, designer, deck machinery supplier, NewRV team…
and with the help of foreign colleagues!!
Design phase

## Slide 19
Matrix of Vessel Functions
As a requirement
Campaign/operation vs. sea state/vessel speed/depth /location/frame-winch-crane/instrumentation
Required combination of given activities, be it simultaneously or during the same campaign
Has been proven to be very useful!
Design phase

## Slide 20
Tow-tank tests
Propulsion tests with stock propeller
Propulsion tests with design propeller
Cavitation tests propeller
Seakeeping tests incl. roll reduction tank
Bubble-sweep down tests
Large effort by Rolls-Royce Marine to design a silent but efficient propeller for a limited draft of 4.8 m.
Design phase

## Slide 21
Building phase
13.02.2019: First Steel cut
27.03.2019: Keel laying

## Slide 22
Building phase

## Slide 23
Building phase

## Slide 24
Building phase

## Slide 25
Please visit: odnature.naturalsciences.be/belgica & belspo.be/NewRV
Website, Facebook, Twitter, etc.
Thank you!
Notes: 25