## Slide 1: ExperiEnce with new MAGS
13.06.2018
Waste Treatment on RV „SONNE“
Lothar Meinders

## Slide 2
Notes: Seit 2004 existiert die Abteilung Forschungsschiffahrt

## Slide 3: Vessels under Operation Briese Research

## Slide 4: Type of waste on board
75 persons 90 days at see  200 cbm not compressed garbarge

## Slide 5: Paper - BEFORE
Compactor Tony Team 75 MC
Upper carriage moves in sea state
volume of cardboard and paper after pressing still too large

## Slide 6: Paper - AFTER
Cardboard shredder and briquettes Mashine MGP MÜTEK
easy fast safe handling
volume of cardboard and paper after pressing very small
Easy Handling of briquettes (could be used as firewood)
Dust succed out with vaccum cleaner

## Slide 7: Glass - BEFORE
Glasscrusher GKF 550 Disperator
Liquids leak and are difficult to clean
very fine glass dust  dust protective mask
weak engine stops at bottle caps
Very loud

## Slide 8: Glass - AFTER
Glasscrusher DT 200 GC DELITEk
large pieces of broken glass – no dust
even champagne bottles are crushed
Very quiet
Easy handling of glass in a 200 Liters Container with garbage bag

## Slide 9: Metal AND PLASTIC - BefORe
DP 20 STRAUTMANN – Metal compactor
slow processing
If several CANS are pressed at the same time, the closing flap opens uncontrollably
Liquids run out - extensive cleaning
IP 20 ICM – compactor
Never Used due to low compressive rate

## Slide 10: METAL AND Plastic - AFTER
Shredder DT 755SR DELITEK
Quick safe handling
high compression rate
large cans or pallets are shredded
200 liters of containers (as with the glass Crusher) catches everything - easy handling

## Slide 11: Wet Garbage
Concept until 2017: Storage in the freezer
Countries of South America, New Zealand, Australia, Alaska, Russia and Japan have not allowed the dumping of wet waste in the port to Protection against epidemics, parasites and foreign pathogens
A waste incinerator was not available because of the stringent emission standards for compliance with “Blue Angel” regulations (German label for high environmentally standard)

## Slide 12: Micro Auto Gasification System (MAGS)
Auto Gasification
is a patented technology which thermally breaks down hydrocarbons into solid carbon and synthesis gas and uses the synthesis gas to fuel the process.
MAGS converts all organic waste, such as plastics, papers, food, cardboards, textiles, wood, used oil, and sludge, into energy , bio-char and water.

## Slide 13: Function of MAGS from Terragon

## Slide 14
Commitment on RV SONNE
New auxiliary engine room was installed 2017
Only Gasification of wet waste and paper every 3 / 4 days (nominal waste input 50 kg / hr)
Low consumption of gas oil (11 l/hr especially for heating up)
Cold exhaust gas (50°C) which fulfill the regulation “Blue Angel”
small amount of ash (BIO char 5% of volume) that can be disposed without problems in all ports

## Slide 15
Regular Maintenance
Burner control, nozzle control and control of the combustion chamber
Free the process air lines to the ash slugs / gas chambers of ash residue
Control of the pneumatic seals and the sliding surfaces of the sliding gates
If necessary, fill up with fuels (sodium carbonate and diesel)
Test run and control of the parameters ports

## Slide 16
experience after one year operation
Broken Mixer Motor
Renewing of Sealing sliding gates
Stuck process water pump
Defective sealing Quench tower
Defective closing mechanism

## Slide 17
Support BY Terragon
Modified Quenchsystem within new insulation
Installation of two duplex Filters
Control all process parameters and their optimization
New type of Process water pump with open impeller
Quick answers
very good documentation
Very Good Support!

## Slide 18
Thank you for your attention
  Questions?

## Slide 19
Questions Loading of MAGS

## Slide 20
Questions char cleaning

## Slide 21
Questions
Specs | V8
Size: | 10.1m3
Weight: | 4,820kg
Capacity (solid waste): | 50 kg/hr
Capacity (sludge/oil) | 20 L/hr
Feeding Lid: | 0.15m3
Feeding: | 15 sec every 10 min Automated for sludge
Char Removal: | Automated
Operation: | 24 hours/day

## Slide 22
Questions
MAGS emissions compared to Quebec Règlement sur l’assainissement de l’atmosphère (RAA chapitre Q-2, r. 4.1) |  |  | 
Parameter | MAGS | RAA Limits | Units
Carbon monoxide | 34 | 57 | mg/m3
Particulate matter | 0,58 | 20 | mg/m3
Hydrogen chloride | <0,6 | 50 | mg/m3
Hydrogen fluoride | <0,028 | - | mg/m3
Dioxins/FuransTEF | 0,0010 | 0,080 | ng/m3
Mercury | 0,56 | 20 | µg/m3
1 - All emission limitations are measured at 11 percent oxygen, 298K, dry basis at standard conditions. 2 - Based on waste formula of 40% plastic (including PVC), 55% celluloid material, 5% moisture 3 - Based on emissions testing performed in December 2014 using MAGS V7 |  |  | 

## Slide 23: Questions