## Slide 1
R/V Bat-Galim - a new governmental research vessel
21st ERVO Annual Meeting June 11-13 , 2019 Hamburg, Germany

## Slide 2
Israel Oceanographic & Limnological Research (Since 1967)
http://www.ocean.org.il
Annual budget: ~ $ 16 million
Staff: ~ 160 scientists (50 PhDs), engineers, technicians and support staff
~ 70 MSc. & PhD. students
~ 75 publications in scientific peer-reviewed journals and 150 Reports
~150 research projects (40 International and 25 National Funds)
> 6500 high school students (lectures, field and laboratory experiments)
National Center of
Mariculture - NCM
Kinneret Limnological Laboratory - KLL
National Institute of Oceanography - NIO
Mediterranean Sea
Sea of Galilee
Red Sea
E. Med. Sea
Red Sea

## Slide 3
IOLR Core Activities:
Oceanographic research - physical, chemical, geological and biological;
Monitoring and assessment of human impacts on marine and coastal ecosystems and resources;
Development of Operational Oceanography -observing and modeling systems to provide timely environmental information and predictions;
Mapping, environmental risks, geo-hazards and multidisciplinary studies - marine surveys, data collection and organization of environmental data bases, process studies;
Operation of the Israel Marine Data Center as the national repository and dissemination facility for oceanographic data and data products.
5 Desalination plants , 650 mcm
5 Power plants
Few fact on the Israeli EEZ & coastal waters
(https://isramar.ocean.org.il)

## Slide 4
Israel Exclusive Economic Zone (EEZ)
The recent (2009) large-scale natural gas (~ 1,000 BCM) and oil discoveries in the deep sea of the Israeli EEZ stressed the need of a National Research Vessel capable of working in the deep EEZ.
On February 2012 - Governmental decision to build/purchase research vessel (budget ~ $ 5 M)
Leviathan
Tamar
Dalit
Tanin
Dolphin
Noa
Aphrodite
Cyprus EEZ
Lebanon EEZ
Egypt EEZ

## Slide 5
Vessel tasks
Deep sea research (Oceanography, Biology, Geophysics, Geology, Geo-chemistry)
Environmental surveys & monitoring
Geo-hazard assessment
Academic research & education
Oil-spill response
Search and recovery

## Slide 6
Hull material | Steel | Max. draft | 3.45 m | Endurance at sea | 14 days
LBP | 34.6m | FB | 3.1m | Operational range | ~ 1,000 nm
LOA | 38.55m | Max speed | 12.7 knots | Propulsion | 2X208 HP jets & single propeller
Max. displacement | 528 ton | Crew + Scientists | 14 (24) |  | 
Deutz Generators | 2X 124 kW |  |  | Propulsion system | 890 KW Deutz engine
Built: 1990
1,000 nm
EEZ
German-built Klein-Klasse support vessel
Purchased from the Israeli Navy June 1st, 2014

## Slide 7
Acoustic tests - Pre. & Post Gondola installation (http://mac.unols.org/reports)
The BAT GALIM was determined to be a relatively quiet platform for MBS data collection.
Propeller cavitation characteristics are good up to 8 knots and no machinery noise was noted that will impact sonar data.
Bubble sweep down impacts were not detected at any time during the acoustic test.
The acoustic levels measured during normal ship operations up to 8 knots are similar to other vessels equipped with mid-depth MBS systems
Post
Pre.
dB
dB
50
40
50
40
dB
Gates Acoustic Services
Post
50
40
R/V Bat Galim
R/V Nautilus
R/V Sikuliaq
R/V Bat Galim
R/V Otter Bay
30 kHz
30 kHz
200 kHz

## Slide 8
Guidelines for setting a modern Research Vessel
The refitting of the Bat Galim into a modern research vessel follows most of the guidelines set in the Science Mission Requirements (SMR) for Regional Class oceanographic vessels that were developed as part of the Academic renewal efforts by the University-National Oceanographic Laboratory System (UNOLS).

## Slide 9
Labs
Telescopic A Frame
2 Cranes
Gondola
Dynamic Positioning
winches
(June 2014-June 2016)
Refitting from military vessel to modern R/V
Acoustic (50kHz) draft meter

## Slide 10
A-Frame: Telescopic, SWL 3t at 5m, 1t at 7m (4m width), tilt 40deg.
20’ Dry Lab
Crane: Palfinger (PK 11001 M) 11 ton⋅meter, Boom Length 10.5m
20’ +1.5 m WET Lab
2 Winches
Crane: 4 ton⋅meter, Boom Length 12.5m
R/V Bat Galim Aft Deck (~ 14 m long X 10 m wide)
Can load 4 X 20’ containers

## Slide 11
R/V Bat Galim: Research Capabilities and other Tasks
Map the sea floor and the water column - Two multibeam systems WD 10 - 7,000 m
Map the sub-bottom in a very high resolution –CHIRP and Sparker (single & multichannel)
Sample the sub-bottom – two systems: Box Core and Piston/Gravity Core (up to 9 m long)
3-D continues current profiling – ADCP system up to 700 m below the vessel
Sample the water column – CTD and Rosetta
Data and sample analysis– Hydrographic lab/Wet/Dry/Isotope/Processing capabilities/Geophysical lab
Operate & deploy autonomous and guided equipment – AUV and ROV
Oil spill response - Spray oil dispersants & clean with oil spill skimmer
Search and recovery of missing aircraft & vessels- Pinger locator, Side scan Sonar, ROV

## Slide 12
High resolution (WD ~< 300 m)
Resolution ~ 20 cm
07 deg. TX by 0.7 deg. RX
Mapping the sea floor and the water column

## Slide 13
Example of submarine deep channels (WD~ 1,700 m)
Deep water sea floor mapping (up to 7,000 m)
Gondola
Receive
Transmit
2 deg. TX by 2 deg. RX

## Slide 15
Monitoring sediment transport and morphological changes on the shelf
4. Subsurface changes

## Slide 16
9 X 3.5 kHz transducers
12kHz transducer
Map the sub-bottom in very high resolution – CHIRP 3260
Example of submarine deep channels
(WD~ 1,440 m) in the EEZ

## Slide 17
Sample the sub-bottom sediments
9 m Piston Core
6m Vibro Core
Woods Hole; USGS
Box Core

## Slide 18
Current magnitude, Training cruise offshore Hadera, June 2016 (Tal Ozer)
ADCP in the Gondola
3-D continues current profiling

## Slide 19
Controls & operates the: navigation, multibeam, ADCP, Chirp, Camera etc.
Hydrographic lab. - Real time data acquisition & processing
Data and sample analysis

## Slide 20
Wet Lab. ~ 18 sq.m.
Dry Lab. ~ 15 sq.m.
Isotope Lab. ~ 2.5 sq.m.
Dry and wet labs

## Slide 21
Split data screen in each room.
Remote displays & processing capabilities in each Lab. & room
Data screen bridge
In each room & Lab.:
Split data screen
High speed intranet connection to main computer to enable individual data processing

## Slide 22
Operate & deploy autonomous and guided equipment – AUV, ROV, mooring buoy's etc.
USBL (LinkQuest TC5000HA)
Seaeye Leopard 3000m ROV
Buoy deployment
Deploy mooring systems
AUV- ECA A18D: 3000m depth, synthetic-aperture-sonar (SAS), camera stereo-pair, sub-bottom profiler, obstacle avoidance system

## Slide 23
Oil spill drill June 2016
Oil spill skimmer
Oil spill dispersant
spill
Bat Galim
Bat Galim control room June 2016
Drone with FLIR
Oil spill drill October 2018
2 X 20’ containers with clean up equipment
Oil spill response

## Slide 24
We hope you join us at sea as part of the EuroFleet
Special thanks for the help and advise from: Larry Mayer; Dwight Coleman; Todd Gregory; Tim Gates; Marisa Yearta; Paul Johnson; Jim Broda and Kongsberg people. IOLR: Gideon Amit ; Dani (Fritzi) Ramot; Michael Erez; Michael Epshtien; Mor Medndelson; Eldad Israeli; Tomer Keter; Mor Kanari; Tzahi Levi;
21st ERVO Annual Meeting June 11-13 , 2019 Hamburg, Germany